- Async v threads
  - thread creation and context switching has overhead
    - The decision often depends on the intended system and architecture your program will be running on.

- Threads
  - State
    - detached – joinable
  - shared buffer
    - mutex
    - lock – unlock
  - dead lock
    - threads get stuck waiting for eachother and hang indefinitely
  - race condition
    - threads are supposed to be executed in a specific order, but due to the scheduling of the threads, they get executed in the incorrect order
      - this can often be caused by external factors, memory or some other non-dterministic factors. Reproducing this error can be very difficult sometimes
  - shared resources
  - callback events
- Input
  - canonical mode
    - .c_lflag &= ~ICANON
      - bitwise and with the inverse of the Icanon flag – truns off canonical mode
    - .c_lflag |= ICANON
    - .c_cc[VMIN] = 1
    - .c_cc[VTIME] = 0
    - in canonical mode a read on the serial port will not return until a new line EOF or EOL
      - read always returns a new line
    - in non-canonical mode a read on the serial port will not wait until the new line
      - the number of bytes read depends on the MIN and TIME settings
        - MIN – sets the minimum number of characters to wait for
          - if zero it returns as many characters as possble
          - if > 0 it waits for that number of characters to be present before returning
        - TIME – sets the amount of time to elapse before the read returns
        - when both are greater than 0, the read returns on whichever is condition is met first